## Slide 1: NAIRR – Sensor Fusion, Estimation, and AI
From separate detections to one estimate

## Slide 2: The Through-Line
Workshop 4.2 gave you separate, instantaneous detections.
Workshop 4.3 turns noisy sensor streams into one confident estimate of the world.
Three threads from Workshop 4.2 we are going to build on today:
  Fusion — sensors in a common coordinate frame
  Tracking — objects across frames
  Control — beyond rule-based or RL
A perception stack that doesn't remember, doesn't fuse, and doesn't connect to control is a demo. Today turns the demo into a system.
2

## Slide 3: Today's Pipeline
3
Five stages: Sense → Fuse → Estimate → Track → Act. The first you built in Workshop 4.2. The other four are today.
FROM 4.2
Sense
Camera and lidar
perception, per frame
L1 · L2
Fuse
Complementary sensors
in one coordinate frame
L3 · L4
Estimate
A state estimate
that lives in time —
the heart of today
L5
Track
Multi-object persistence
across frames
L6 – L8
Act
Closed-loop control,
classical through learned
We close with a brief look at the modern AI frontier — BEV deep fusion, learned filters, end-to-end driving.

## Slide 4: Where We Stopped
4
In Workshop 4.2, the camera notebook ran YOLO on every frame independently. The system had no memory.
A detection is a noisy guess about one frame. Useful, but not enough to plan or control on.
What we need is an estimate, a best guess plus uncertainty, that survives across frames.
Frame t
Frame t+1
Frame t+2

## Slide 5: Why Fuse?
5
No single sensor sees everything. Camera, lidar, and radar measure different parts of the state (fusion is about complementarity, not only redundancy)
Camera
Semantics, color, texture
Strengths
Cheap and information-rich
Reads signs and brake lights
Mature, well-understood
Limits
No native depth
Weather and lighting weak
Lidar
3D geometry, range
Strengths
Dark-robust, ambient-independent
Centimeter-accurate geometry
Direct 3D point cloud
Limits
No semantics
Sparse and expensive
Radar
Velocity (Doppler)
Strengths
Direct velocity measurement
Most weather-robust of the three
Long range
Limits
Low resolution
Fuzzy shapes, not silhouettes
They measure different parts of the state. Fusion is about complementarity data.

## Slide 6: Fusion Taxonomy
6
Three places in the pipeline to combine sensor data, each with its own tradeoff between accuracy and robustness.
EARLY
Raw
Before detection
Example
Point painting:
lidar points colored
by camera pixels
Strength
Most information
preserved
Weakness
Brittle;
calibration-hungry
MID
Features
Inside learned features
Example
BEV deep fusion
(modern stacks)
Strength
Best in deep models
Weakness
Hard to debug
LATE
Objects
After per-sensor detection
Example
Track-level fusion
via Kalman filter
Strength
Modular;
failure-graceful
Weakness
Information lost
before fusion
The tradeoff: modular survives sensor dropout; end-to-end achieves higher accuracy on clean data. Production stacks tend toward late or hybrid; research papers tend toward early.

## Slide 7: Calibration & Time Sync
10
The most unglamorous prerequisite in the fusion stack. Skip it, and everything downstream is silently wrong.
Frames
Each sensor measures in its own coordinate system. Fusion means transforming everything into one common frame.
Calibration
Intrinsic — one sensor’s focal length and distortion.
Extrinsic — the transform between sensors.
Time sync
Sensors fire at different instants. Fuse a stale return with a fresh detection and you fuse two different worlds.
Why one degree matters
Extrinsic angle error projected to ground position error
Angular error | Position error at 10 m | at 20 m
1° | ~17 cm | ~35 cm
2° | ~35 cm | ~70 cm
5° | ~87 cm | ~175 cm
AND TIME COUNTS TOO
100 ms of latency ≈ 3 m of misalignment at highway speed