## Slide 1: NAIRR – Sensor Fusion, Estimation, and AI
Presentation 3 — Acting on the World

## Slide 2: From Perception to Action
We can now estimate and track the world. So what?
Perception is never the goal — it exists to enable a decision. The loop only closes when our state estimate becomes a steering angle and a throttle command.
Sense → Fuse → Estimate → Track → Act
The rest of today is the 'Act' stage: turn a tracked, uncertain world into safe motion — first by following a path, then by not hitting anything.
2
Sense · Fuse · Estimate · Track · Act
N4 · Path Track
Notes: Transition slide. The point: a perfect tracker that never acts is still just a demo (callback to slide 2). Control is where perception earns its keep. Set up the two pieces: path tracking (steering) and the safety layer (longitudinal / braking).

## Slide 3: Following the Path
3
Given a reference path, how do we steer onto it? Two classical controllers — no learning required.
THE JOB
Path tracking
path → steering angle
Input
A reference path and
the vehicle’s state
Output
A steering command,
every timestep
OPTION A
Pure Pursuit
aim ahead
Idea
Pick a lookahead point
on the path; steer
toward it
Feel
Simple, smooth,
forgiving
OPTION B
Stanley
kill cross-track error
Idea
Correct heading and
lateral offset together
Feel
Tighter tracking,
less corner-cutting
Both are pure geometry plus a gain or two. You implement and tune them against a real path in N4.
Sense · Fuse · Estimate · Track · Act
N4 · Path Track
Notes: Pure pursuit: imagine driving by always aiming at a point a fixed distance ahead on the lane — lookahead distance is the key knob (short = twitchy, long = lazy). Stanley adds an explicit cross-track term, so it hugs the path harder. Both are still used in production.

## Slide 4: Don’t Hit Things
4
Steering keeps us on the path; a separate safety layer keeps us off the car in front. It runs on the tracks we built.
FORECAST
Time-to-collision
how many seconds?
Idea
Project tracks forward
along our path
Output
TTC — seconds until
impact if nothing
changes
NORMAL
Adaptive cruise
keep a gap
Idea
Match the lead car’s
speed
Rule
Hold a distance that
grows with speed
DANGER
Emergency brake
override
Trigger
TTC below threshold
Action
Full brake — ignore
cruise, ignore
comfort
Estimation and tracking feed the controller. This safety glue is the beating heart of the N5 capstone.
Sense · Fuse · Estimate · Track · Act
N4–N5 · Safety
Notes: This is the piece that ties perception to consequences. TTC turns tracked velocities into a scalar risk; adaptive cruise handles the normal case; the emergency-brake override is what the live demo will toggle. Foreshadow: turn it off and watch a crash.

## Slide 5: The Capstone: One Loop, Every Piece
5
N5 is not a new topic — it’s every subsystem you built, wired into a single closed loop on real data.
REAL DATA
KITTI drive
a real ego trajectory
Source
Real vehicle path from
KITTI drive 0005
Why
Grounded motion, not
a toy straight line
CLOSED LOOP
It runs itself
perception drives control
Loop
Sense → estimate →
track → plan → act
→ move → repeat
Why
Errors compound —
like real driving
EMERGENT
Crash or avoid
behavior, not script
Idea
Outcomes emerge from
the knobs you set
Why
No outcome is
hard-coded
Every notebook becomes one subsystem of a single running simulator — fuse, estimate, track, plan, act.
Sense · Fuse · Estimate · Track · Act
N5 · BEV Sim
Notes: Reassure them this is synthesis, not new material. Each box maps to a notebook they just did. The novelty is the closed loop: control changes the next frame's perception, so small errors compound — exactly why estimation and a safety layer matter.

## Slide 6: Live Demo: Tune the Knobs
6
This is your turn. A bird’s-eye simulator with live sliders — change a setting and watch the outcome change instantly.
KNOBS
What you control
Try
Controller & lookahead
Collision avoidance on/off
TTC threshold
Antagonist behavior
Sensor noise / blackout
WATCH
What you see
Panels
BEV ego-centered view
Estimate vs. ground truth
Live TTC trace
Crash / clearance readout
THE MOMENT
Make it crash
Demo
Cut-in with avoidance OFF
→ collision
Then
Avoidance ON → it brakes
Blackout the sensor →
'didn’t see it coming'
Sliders are live — no re-render, no Run button. This is the hands-on; spend your time here.
Sense · Fuse · Estimate · Track · Act
N5 · Hands-on
Notes: Drive the demo live: start clean (no crash), turn avoidance off and trigger a cut-in to get a collision, turn it back on to show the brake, then blackout the sensor mid-approach for the 'it didn't see it coming' moment. Then hand off — let them break it themselves.

## Slide 7: Classical → Learned: BEV Deep Fusion
7
Everything today was modular and hand-built. The frontier fuses earlier and learns the fusion itself.
TODAY
Late fusion
what you built
How
Per-sensor detection,
then combine objects
(Kalman, association)
Strength
Modular, debuggable,
fails gracefully
FRONTIER
BEV deep fusion
the 'MID' box, paid off
How
Fuse camera + lidar
features in a shared
bird’s-eye grid
Strength
Learned end-to-end;
higher ceiling
COST
Nothing’s free
the tradeoff
Needs
Data, compute,
calibration
Loses
Interpretability —
hard to debug
Remember the fusion taxonomy? BEV deep fusion is the 'MID' box — now the dominant research direction.
Sense · Fuse · Estimate · Track · Act
Frontier
Notes: Tie back explicitly to the early/mid/late taxonomy slide. BEV deep fusion projects all sensors into a common bird's-eye feature grid and lets a network do the combining — the same BEV view your capstone draws, but learned rather than hand-built.

## Slide 8: Learned Filters & End-to-End Driving
8
The same 'replace hand-tuning with learning' pressure reaches estimation and control too.
ESTIMATION
Learned filters
neural / differentiable
Idea
Learn the dynamics and
noise (Q, R) from data
instead of tuning
Keeps
The predict/correct
structure you know
CONTROL
End-to-end
pixels → controls
Idea
One network from raw
sensors to steering
Drops
The explicit pipeline
in between
WHY MODULAR LIVES
Accountability
safety-critical reality
Tension
End-to-end wins on
clean-data accuracy
But
Modular stacks can be
verified and debugged
— why they persist
The pendulum of the field: end-to-end accuracy versus modular accountability.
Sense · Fuse · Estimate · Track · Act
Frontier
Notes: Keep this honest: end-to-end is not strictly 'better.' It excels on data it has seen but is hard to verify, so safety-critical autonomy still leans modular. The skills they built today (explicit estimation, tracking, control) are exactly what makes a stack auditable.

## Slide 9: Recap: A Stack You Built From Scratch
9
Five stages, five notebooks, one loop. Here’s the whole arc — and what you can now do at each stage.
4.2
Sense
Detect per frame
(camera + lidar)
N1
Fuse
Project sensors into
one coordinate frame
N2
Estimate
Kalman filtering — a
state that lives in time
N3
Track
Many objects, kept
alive through occlusion
N4 · N5
Act
Path tracking + safety,
closed loop on real data
You built a perception-to-control stack from scratch — now go break the simulator.
Sense · Fuse · Estimate · Track · Act
N1 – N5
Notes: Land the plane: each box is something they implemented, not just saw. Restate the through-line from slide 2 — a stack that remembers, fuses, and acts. Then send them into the 2-hour hands-on block, ending on N6.