## Slide 1: Capstone: Navigate the Real Scene
Every subsystem, one closed loop, real obstacles

## Slide 2: One loop, every piece
N1 fuse -> N2 estimate -> N3 track -> N4 act, wired into one running loop on the real KITTI drive.
• No new theory — this is integration
• Real ego route, real-derived obstacles
• Emergent thread-or-clip outcomes

## Slide 3: The obstacles are real (in spirit)
N3 detects cars at realistic sizes; we place them on the route so the ego must thread them.
• Car ~ 4.2 x 1.8 x 1.5 m (from N3's clustering)
• Perceived with noise, then tracked
• The ego steers around the tracked positions

## Slide 4: Steering around: potential field
Each obstacle in the corridor pushes the ego sideways; it weaves and re-centers.
• One gain to tune (the avoidance strength)
• Pure-pursuit steer + repulsion bias
• Emergency brake if a car is dead-ahead

## Slide 5: The bird's-eye view
Ego-relative — forward up, you at the bottom — exactly N3's BEV.
• Green = road, red = obstacle
• Tracked detections shown with uncertainty
• The real, curved KITTI route

## Slide 6: Live demo: tune the knobs
Set the controls, render, watch it thread or clip.
• Avoidance gain, lookahead, speed
• Number of cars / layout seed
• Sensor noise / blackout

## Slide 7: What you built
A perception-to-control stack on real data — sense, fuse, estimate, track, act.
• Modular and auditable
• Each piece swappable behind a clean interface
• The frontier learns these pieces end-to-end